Dielectrophoretic Placement of Quasi-Zero-, One-, and Two-dimensional Nanomaterials into Nanogap for Electrical Characterizations

Supporting Information

The dielectrophoretic force acting on a homogeneous dielectric material is given by the well-known analytical expression:, where E is the magnitude of the electric field. fCM is the Clausius-Mossotti factor, defined as , where  and  represent the complex permittivity of the particle and that of the suspending medium, respectively. The complex permittivity is described by an equation,, where , ,  are the permittivity, conductivity, and angular frequency of applied electric field, respectively. The direction of DEP motion depends on the sign of the real part of the Clausius-Mossotti factor, Re[fCM]. When the value of Re[fCM] is positive (negative), particles move towards the high (low) electric field region. Figure S1 represents the value of the real part of Clausius-Mossotti factor as function of frequency for the case of (A) PbSe QDs (εp=250 ε0 , σp=2×10-2 S/m) suspended in a toluene solution (εp=2.379 ε0 , σp=5×10-10 S/m), and (B) polyaniline nanofibers (εp=2 ε0 , σp=2×103 S/m) suspended in deionized water (εp=80 ε0 , σp=10-6 S/m) (see Table S1). From the simulation results in Figure S1, it is clear that, at low frequencies, the Re[fCM] reveals a positive value, causing an attractive DEP force. Thus the specified, constant frequency of 1 MHz AC voltage selected in our study (for the cases of PbSe QDs and polyaniline nanofibers) is definitely under an attractive force regime. In addition, the value of Re[fCM] decreases gradually with increasing the value of the operated frequency. In the case of polyaniline nanofibers, the Re[fCM] reduces to be negative in a frequency higher than 1011 Hz.

Figure S1. The real part of the Clausius-Mossotti factor as a function of frequency for the cases of (A) PbSe QDs, and (B) polyaniline nanofibers.

|  | ε (F/m) | σ (S/m) | Reference |
| --- | --- | --- | --- |
| PbSe | 250 ε0 | 2×10-2 | Science 2005, 310, 86 |
| Toluene | 2.379 ε0 | 5×10-10 | CRC handbook of chemistry and physics |
| Polyaniline nanofiber | 2 ε0 | 103 | ACS Nano 2011, 5, 1541 |
| DI water | 80 ε0 | 10-6 | Nano Lett. 2009, 9, 2260 |

Table S1. The parameters of the DEP force, and their corresponding references.

In the case of rGO devices, the frequency of 300 kHz was chosen, according to a previous report (See ACS Nano 2009, 3, 1729). In this reference, we have got an evidence to guarantee the occurrence of a positive DEP force under this specific frequency.